## Slide 1: Monte Carlo Algorithm for Leakage Optimization Based on Input Vector Control
Yuan Cao

## Slide 2: Contents
Problem definition --- Input Vector Control
Algorithm and implementation
Results and Discussion
Conclusion

## Slide 3: Input Vector Control
A method for reducing leakage power consumption
Input vector(A,B,Ci) | Output(S,Co) | Leakage/nA
000 | 00 | 76.97
001 | 01 | 104.60
010 | 01 | 126.48
011 | 10 | 124.12
100 | 01 | 146.35
101 | 10 | 126.51
110 | 10 | 146.13
111 | 11 | 105.73
FA
A
B
Ci
S
Co
FA
FA
FA
FA
A0
B0
A1
B1
A2
B2
A3
B3
S0
S1
S2
S3
C0
C4
Extracted from Cadence GSCLIB090 ADDFXL

## Slide 4: Finding the best input vector
NP-Complete problem
  Heuristic algorithm
  Random search
Existing Algorithms
  Linear programming
  Dynamic programming
  2-SAT
  Random searching
Problems
  Slow
  Sub-optimal result

## Slide 5: Random search
A large class of algorithms based on random numbers
Crude and simple, but can be sometimes effective
Simplest random search:
  n=64 inputs
  Number of state N=1.845×1019
  Random search ~108 states

## Slide 6: Improvement: Simulated Annealing
Analogue of thermodynamics problem
Temperature T: characterizes the randomness

## Slide 7: Simulation model
Hierarchical model for simulating combinational logic
Input | Output | Leakage/nA
00 | 1 | 1.37
01 | 1 | 28.92
10 | 1 | 52.53
11 | 0 | 1.259
NAND

## Slide 8: Implementation
Top-level
Circuit
Input Vector
Minimize_Leakage(C, n)
  input[] = random(n);
  leak = evaluate(input);
  T = T0;
  while(T<Tfinal){
  index = random(n);
  input[index].flip();
  new_leak = evaluate(input);
  if(new_leak < leak){
  leak = new_leak;
  // save input vector
  }
  else{
  prob = e-(new_leak-leak)/T;
  if(random() < prob){
  leak = new_leak;
  }
  else{
  // restore
  input[index].flip();
  continue;
  }
  }
  T = (1 - a) * T;
  }

## Slide 9: Extra heuristics
Since only one bit is flipped, possibility of getting stuck
  Example: T=0.5
  0000000011000000 10
  0000000010000000 15
  0000000001000000 15
  0000000000000000 8
Solution: Do relaxation after several iterations
  Enumerate and try all possible two-bit flips

## Slide 10: Results and Discussion
Everything implemented in Java
  2535 lines of code
NOT, AND, OR, NAND, NOR, XOR, FA, etc. tens of gates extracted from GSCLIB090 technology library.
Tested on a number of benchmark circuits

## Slide 11: Simulated Annealing
16-bit Adder

## Slide 12: Benchmark
Circuit | Inputs | Gate count | Min. Leakage(nA) | Time(s) (By bruteforcing) | Avg. annealing Leakage(nA) | Time(s) (By annealing) | Ratio
Adder-4 | 9 | 4 | 307.9 | 0.1 | 307.9 | 0.1 | 1.00
C17 | 5 | 6 | 35.4 | 0.1 | 35.4 | 0.1 | 1.00
C432 | 36 | 160 | 3360.6 | - | 3389.1 | 1.0 | 1.008
C880 | 60 | 383 | 9716.7 | - | 9815.9 | 6.0 | 1.010
C1355 | 41 | 546 | 11081.9 | - | 11081.9 | 5.0 | 1.00
C3540 | 50 | 1669 | 52588.5 | - | 52588.5 | 25.0 | 1.00
C6288 | 32 | 2416 | 75939.3 | - | 75939.3 | 22.0 | 1.00
C7552 | 207 | 3512 | 1.05×105 | - | 1.07×105 | 439.0 | 1.019
ISCAS85 Benchmark circuits

## Slide 13: Conclusion
An improved version of random search for input vector control is developed based on widely-used simulated annealing algorithm
The effectiveness and validity of the algorithm is verified.
Possible further improvements
  Use more efficient programming language such as C++

## Slide 14: References
Gao, Feng, and John P. Hayes. "Exact and heuristic approaches to input vector control for leakage power reduction." Computer-Aided Design of Integrated Circuits and Systems, IEEE Transactions on 25.11 (2006): 2564-2571.
Chang, Xiaotao, et al. "Fast algorithm for leakage power reduction by input vector control." ASIC, 2005. ASICON 2005. 6th International Conference On. Vol. 1. IEEE, 2005.
Cheng, Lei, et al. "A fast simultaneous input vector generation and gate replacement algorithm for leakage power reduction." Proceedings of the 43rd annual Design Automation Conference. ACM, 2006.
Aloul, Fadi A., et al. "Robust SAT-based search algorithm for leakage power reduction." Integrated Circuit Design. Power and Timing Modeling, Optimization and Simulation. Springer Berlin Heidelberg, 2002. 167-177.
Halter, Jonathan P., and Farid N. Najm. "A gate-level leakage power reduction method for ultra-low-power CMOS circuits." Custom Integrated Circuits Conference, 1997., Proceedings of the IEEE 1997. IEEE, 1997.

## Slide 15: Thanks!