## Slide 1: Monte Carlo Algorithm for Leakage Optimization Based on Input Vector Control
Yuan Cao

## Slide 2: Contents
Problem definition --- Input Vector Control
Random algorithm
Results and Discussion
Conclusion

## Slide 3: Input Vector Control
A method for reducing leakage power consumption
Input vector(A,B,Ci) | Output(S,Co) | Leakage/nA
000 | 00 | 76.97
001 | 01 | 104.60
010 | 01 | 126.48
011 | 10 | 124.12
100 | 01 | 146.35
101 | 10 | 126.51
110 | 10 | 146.13
111 | 11 | 105.73
FA
A
B
Ci
S
Co
FA
FA
FA
FA
A0
B0
A1
B1
A2
B2
A3
B3
S0
S1
S2
S3
C0
C4
Result from Cadence GSCLIB090 ADDFXL

## Slide 4: Pseudo-Boolean function
n inputs = 2n terms to be summed
Impossible to bruteforce for large circuit

## Slide 5: Finding the best input vector
NP-Complete problem
  Heuristic algorithm
  Random search
Existing Algorithms
  Linear programming
  Dynamic programming
  2-SAT
  Random searching
Problems
  Slow
  Sub-optimal result

## Slide 6: Random search
A large class of algorithms based on random numbers
Crude and simple, but can be sometimes effective
Simplest random search:
  n=64 inputs
  Number of state N=1.845×1019
  Random search ~108 states

## Slide 7: Improvement: Simulated Annealing
Analogue of thermodynamics problem
Temperature T: characterizes the randomness

## Slide 8: Simulation model
Hierarchical model for simulating combinational logic
Input | Output | Leakage/nA
00 | 1 | 1.37
01 | 1 | 28.92
10 | 1 | 52.53
11 | 0 | 1.259
NAND

## Slide 9: Implementation
Top-level
Circuit
Input Vector
Minimize_Leakage(C, n)
  input[] = random(n);
  leak = evaluate(input);
  T = T0;
  while(true){
  index = random(n);
  input[index].flip();
  new_leak = evaluate(input);
  if(new_leak < leak){
  min_leak = new_leak;
  // save input vector
  }
  else{
  prob = e-(new_leak-leak)/T;
  if(random() < prob){
  leak = new_leak;
  }
  else{
  // restore
  input[index].flip();
  }
  }
  T = (1 - a) * T;
  }

## Slide 10: Extra heuristics
Since only one bit is flipped, possibility of getting stuck
  T=0.5
  0000000011000000 10
  0000000010000000 15
  0000000001000000 15
  0000000000000000 8
Solution: Do relaxation after several iterations
  Enumerate and try all possible two-bit flips

## Slide 11: Results and Discussion
Everything implemented in Java
  2535 lines of code
NOT, AND, OR, NAND, NOR, XOR, FA, etc. tens of gates extracted from GSCLIB090 technology library.
Tested on a number of benchmark circuits

## Slide 12: Simulated Annealing
16-bit Adder

## Slide 13: Benchmark
Circuit | Inputs | Gate count | Min. Leakage(nA) | Time(s) (By bruteforcing) | Avg. annealing Leakage(nA) | Time(s) (By annealing) | Ratio
Adder-4 | 9 | 4 | 307.9 | 0.1 | 307.9 | 0.1 | 1.00
C17 | 5 | 6 | 35.4 | 0.1 | 35.4 | 0.1 | 1.00
C432 | 36 | 160 | 3360.6 | - | 3389.1 | 1.0 | 1.008
C880 | 60 | 383 | 9716.7 | - | 9815.9 | 6.0 | 1.010
C1355 | 41 | 546 | 11081.9 | - | 11081.9 | 5.0 | 1.00
C3540 | 50 | 1669 | 52588.5 | - | 52588.5 | 25.0 | 1.00
C6288 | 32 | 2416 | 75939.3 | - | 75939.3 | 22.0 | 1.00
C7552 | 207 | 3512 | 1.05×105 | - | 1.07×105 | 439.0 | 1.019

## Slide 14: Conclusion
An improved version of random search for input vector control is developed based on widely-used simulated annealing algorithm
The effectiveness and validity of the algorithm is verified.
Possible further improvements
  Use more efficient programming language such as C++

## Slide 15: Thanks!